## Slide 1
Evolution In Gas Detection

## Slide 2: The GX-3R The Smallest and Lightest 4-gas Monitor
H: 2.55”
W: 2.2”
D: 1.02”
And it weighs only 3.52 ounces!

## Slide 3: Size Matters In the “Breathing Zone”
“The breathing zone is within a ten inch radius of the worker's nose and mouth. OSHA requires that worker exposure monitoring air samples be collected in the breathing zone. Air sampling filters may be attached to the collar or lapel.”
GX-3R
So small and light, the GX-3R clips comfortably in the breathing zone.

## Slide 4: Simultaneously Monitor 4 Gasses
All gas readings displayed
CO – Carbon Monoxide
Dual sensor for CO and H2S in one channel
The GX-3R monitors:
Dual filament design gives added silicone poisoning resistance to LEL sensor
Eliminate H2 interference with CO readings with optional H2 compensated O2 sensor
LEL – Combustibles
O2 – Oxygen
GX-3R
(H2 compensated CO sensor available)
Lead free electro-chemical sensor design gives O2 sensor a 3-5 year lifespan

## Slide 5: Sensors
GX-3R
Sensors are field replaceable
(as easy as changing a clock battery)
Can be configured with interchangeable combos to detect a multitude of gasses
Long-lasting with a 3-year warranty

## Slide 6
GX-3R
Easily identify workers using instruments that have not been calibrated, bump tested, or have been in alarm. Red LED’s flash every 30 seconds.
Non-compliance Indicator

## Slide 7: GASCO Calibration Gas Single Gas Detector Verification
30 Bumps Per Cylinder
No hazardous material shipping cost
A Functional “Bump” test should be performed before each use
Many single gas mixes available
If you don’t check – you don’t know
Make Certain Your Gas Detector Works!

## Slide 8: Large LCD Auto-backlit Display
Full dot LCD display is easy to read even in adverse conditions
GX-3R

## Slide 9: Concussion Resistant
The GX-3R has been drop-tested from over 23 feet.
It can handle the conditions of your rugged work environment
GX-3R

## Slide 10: Removable Rubber Boot
The removable rubber boot adds impact protection, can be removed when cleaning and replaced if necessary.
GX-3R
Low profile alligator clip rotates 360°. Comfortably view the instrument display from a variety of positions.
Alligator Clip

## Slide 11: IP-66 / IP-68 Rating
GX-3R
The GX-3R is IP-66 rated because it can withstand jets of water
It is also IP-68 rated because it can withstand submersion in water
Critical for withstanding harsh industrial environments
The first digit shows that it is dust proof
The second digit shows it is waterproof

## Slide 12: 3 Year Warranty
The GX-3R has a 3 year warranty
GX-3R
The warranty covers workmanship of the device
AND the sensors.

## Slide 13: 3 Adjustable Alarm Levels
Three adjustable alarm points let you customize your instrument to fit your needs.
GX-3R
Revert back to standard factory settings any time.

## Slide 14: 3 Alarm Types
Visual LED light indicators Alert you to gas, low battery, and failure alarms
Audible 95 decibel buzzer Buzzer sounds for gas alarms, malfunctions, low battery voltage, and as an indicator
Vibration An internal motor vibrates for gas alarms, unit malfunctions, and as an indicator
GX-3R

## Slide 15: 2 Button Operation
2 Glove -friendly Buttons
GX-3R
Easy to use!

## Slide 16
GX-3R
Rechargeable Lithium-Ion Battery
Lithium Ion battery gives 25 hours of continuous operation minutes, with a complete recharge in 90.
It has an easy and convenient charging cable, no cradle required!

## Slide 17: SDM 3R Calibration Station
GX-3R
Charge, bump test, calibrate and alarm test instruments using less calibration gas
Automatically schedule tests
Bank up to 10 units with tubeless connection
Access instrument data via USB or ethernet

## Slide 18: High Capacity Data Logging
The GX-3R automatically logs data every 5 minutes for 300 hours of measurement. (note: logging interval can be changed in settings)
Infrared Communication Port
Transfer data from the instrument to a PC with a USB/IR adaptor, no cradle required.
GX-3R

## Slide 19: RP-3R Sampling Pump
GX-3R
Clip-on sampling pump has a 50’ range and independent power supply
Continuously operates for 10 hours
Eco mode will operate up to 16 hours

## Slide 20: Lunch Break Mode
GX-3R
Retain TWA and PEAK values from last use to pick up where you left off.
Stealth Mode
Set the alarm to notify silently—perfect for law enforcement and other applications

## Slide 21: Low Cost of Ownership
The GX-3R is a complete instrument. It is easy to maintain and is NOT disposable.
Long lasting sensors, low parts replacement costs, plus a history of long-term product support makes this the best value of any 4-gas instrument
GX-3R

## Slide 22: 9 Languages
GX-3R
Available in 9 languages:
English
日本語 (Japanese)
Español (Spanish)
Deutsch (German)
Français (French)
Italiano (Italian)
Pусский (Russian) 中文 (Chinese)
한국어 (Korean)

## Slide 23: The GX-3R
GX-3R

## Slide 24: 2 Models—Depending on Need
Compliance 4-gas model
GX-3R
Worlds smallest and lightest 4-gas monitor
Impact, water, & dust resistant
3 year Warranty
GX-3R Pro
  4-gas plus extra slot for toxic or IR sensor
  Wireless communication with mobile app
  Man-down and panic alarms
  Alkaline/Rechargeable option
5-gas pro model

## Slide 25
GX-3R User Training

## Slide 26
Turn on the GX-3R by pressing and holding the POWER MODE button until you hear one beep
Turn on

## Slide 27
Press the POWER/MODE button to perform calibration.
Cal Reminder
Acknowledge and use
Perform a calibration
Press AIR button to continue without performing a calibration
If your instrument is past its 30 day calibration limit, you will see a CAL-LMT reminder at start-up

## Slide 28
After warm-up, the normal screen will appear.
Normal Mode

## Slide 29
Fresh Air
To perform a fresh air adjustment, make sure you’re in a fresh air environment.

## Slide 30
Press and hold the AIR button
Fresh Air

## Slide 31
When prompted, release the AIR button
Fresh Air
The GX-3R will beep once and return to normal mode after the fresh air adjust is complete

## Slide 32
To reset the instrument, go to a safe location. Once the readings return to fresh air values, then press the POWER/MODE button.
Alarm
In the event of an alarm, the GX-3R’s visual, audible and vibration alarms will alert you.
The readout will identify which sensor is in alarm.
The visual, audible, and vibration alarms will stop.

## Slide 33: Display Mode
To enter display mode, press and release the Power Mode button

## Slide 34
You will know you are in display mode if you see a display mode menu title on the bottom of your screen
Display mode vs. Normal Operation
PEAK
STEL
TWA
HC GAS LIST
USER ID
STN ID
CAL DATA
BUMP DATA
TEMPERATURE
ALARM-PT
To return to normal operation, scroll all the way through the display menu using the AIR button, or wait 20 seconds and the GX-3R will automatically return to normal mode

## Slide 35
Charging the instrument
Plug the charger into the instrument. A full charge takes 3 hours, and will power the instrument up to 25 hours.
A 30 minute charge will provide 8 hours of operation time.
Once the GX-3R is charged, the light will go from orange to green
Multi-unit AC Adapter is available (#49-0134)

## Slide 36
Downloading Data
Three methods to downloading data from the GX-3R
IrDA cable to PC
SDM-3R to PC
SDM-3R to flash drive to PC

## Slide 37
IrDA cable to PC
Launch the GX-3R Datalogging program
Align the infrared ports
Turn on GX-3R
IrDA Cable
For More detailed instructions: www.gasdetecting.com/files/GX3R_IrDA_to_PC.pdf

## Slide 38
SDM-3R to PC
Launch the SDM-3R PC Controller
Place GX-3R in the SDM-3R docking station
Turn on SDM-3R
SDM-3R to PC
For More detailed instructions: www.gasdetecting.com/files/SDM3R_to_flashdrive_to_PC.pdf

## Slide 39
SDM-3R to Flash drive to PC
Insert flash drive into the SDM-3R and press COPY
Launch the SDM-3R PC Controller
Insert flash drive into the computer’s USB slot
Flash drive
For More detailed instructions: www.gasdetecting.com/files/SDM3R_to_PC.pdf

## Slide 40
RP-3R Attachable Pump

## Slide 41
RP-3R Pump
Place the GX-3R right bottom first (as illustrated above) and then seat the left side until the clip latches.

## Slide 42
RP-3R Pump
The attachable probe has a dust filter to ensure the quality of your samples
The inlet filter housing contains a hydrophobic filter

## Slide 43
RP-3R Pump
Low flow alarm
If the sample line is blocked, the amber flow LED will flash and the buzzer with intermittently sound

## Slide 44
RP-3R Pump
Other Alarm Types

## Slide 45
Turn off the GX-3R by pressing and holding the POWER MODE button for approximately 5 seconds
Turn off

## Slide 46
SDM-3R Calibration Station

## Slide 47
SDM-3R: Gas Ports
Air port:
Dust Filter
Gas 1:
4 gas mix
Gas 2:
Not used
Gas 3
Not used

## Slide 48
SDM-3R: USB port
USB port

## Slide 49
SDM-3R: Rear ports
AC power
Ethernet
PC Connection

## Slide 50
Connect Cylinder to SDM-3R
Connect a 4 gas mix cylinder into “Gas 1 “ port.
Make sure to use a demand flow regulator

## Slide 51
SDM-3R: GX-3R Placement
Plug in power adaptor and turn on the SDM-3R
Make sure the GX-3R is powered off before installing into the SDM-3R
When placing the GX-3R into the docking station, remember to have the yellow tab engaged upwards

## Slide 52
Turn on
If an automatic test is set up to occur, it will start as soon as the GX-3R is connected to the SDM-3R
Close the red door completely, the GX-3R will turn on automatically
When the GX-3R is connected to the SDM-3R, the GX-3R’s date and time are automatically updated to the SDM-3R’s current time and date

## Slide 53
Bump Test
Press the BUMP button to start bump test
Note: Verify that the appropriate calibration gas cylinder is connected to the gas 1 fitting on the left side of the SDM-3R

## Slide 54
Bump Test
During the bump test, the GX-3R’s screen will display the current gas readings

## Slide 55
Bump Test
Once a bump test is complete, the LCD screen will alternate between the gas concentration and pass/fail status (shown as P or F on screen) for each sensor.
The “BUMP” LED light on the SDM-3R will be green when a bump test passes.
The GX-3R will shut off automatically after successful bump test.

## Slide 56
Bump Test
If the bump test fails, ”BUMP” LED light is red. The SDM-3R will then automatically perform a calibration
The LCD screen will alternate between the gas concentration and pass/fail status (shown as P or F on screen) for each sensor for both bump test and calibration
If calibration is successful, the GX-3R will automatically power off

## Slide 57
Calibration
Press the CAL button until you hear the pump to start calibration
Make sure calibration gas concentrations match values shown on display

## Slide 58
Calibration
During calibration, the display shows current gas readings.
Calibration will take approximately 90 seconds.

## Slide 59
Calibration
Once calibration is complete, the LCD screen will alternate between the gas concentration and the letter “P” for pass or an “F” for fail for each sensor
The “CAL” LED light on the SDM-3R will be green when calibration is passed
“CAL” LED light is red if there if a failure. The GX-3R will power off after a successful calibration

## Slide 60
Setting Date/time
Insert GX-3R into the SDM-3R docking station
Press POWER

## Slide 61
Setting Date/time
Press EDIT/ENTER to enter settings menu
Press BUMP to scroll to date and press EDIT/ENTER

## Slide 62
Setting Date/time
Use BUMP and CAL to scroll to the date or time, and press EDIT/ENTER
Use BUMP and CAL to change the value, and press EDIT/ENTER to accept changes.

## Slide 63
Removing from SDM-3R
Release the tab on the red door
Remove the GX-3R

## Slide 64: Training Resources
SDM-3R Cal Station Poster
Ships with each SDM-3R

## Slide 65: Training Resources
YouTube GX-3R Play List
  https://www.youtube.com/playlist

## Slide 66: Training Resources
GX-3R webpage