## Slide 1: World Leader In Gas Detection and Sensor Technology

## Slide 2: Company Background
Founded in 1994
Partnered with Riken Keiki
  Leader In Gas Detection & Sensor Technology for over 75 years
California Corporation
Average employee gas detection experience is 12 years

## Slide 3: 65 Years of Milestones
1938
Worlds first combustible interferometer
1969
World’s first
2 gas monitor
LEL, O2
GX-3
1978
World’s first
3 gas monitor
LEL, O2, CO
Model 1641
1980
Pocket size single gas
OX/CO/HS-80
1982
World’s first belt worn
3-gas
GX-82
1983
Portable IR
for CO2
RI-411
1984
Portable IR for Freons
RI-413

## Slide 4: Milestones
1986
World’s first
belt worn 4 gas monitor
GX-86
1990
Portable
super toxic
SC-90
1994
Portable 4 gas with datalogging
& autocal
GX-94
1995
World’s first
6 gas portable
EAGLE
1997
World’s first wrist worn
GasWatch
2001
World’s smallest
4 gas
GX-2001
2003
Smallest tri-mode
portable
GX-2003

## Slide 5: Sensors
Manufactured not purchased
Enormous sensor manufacturing capacity
Over 500,000 sensors produced each year
Large testing capacity
Aged and tested for 1 to 3 months
ISO 9001:2000 & 14001 (Riken Keiki), ISO 9001:2000 (RKI)

## Slide 6: The GX-2009
Evolution In Gas Detection
INTRODUCING

## Slide 7
All gas readings displayed
GX-2009

## Slide 8
3 Large visual alarms on 3 sides
GX-2009

## Slide 9
2 audible alarms ports, 95 dB
GX-2009

## Slide 10
2 glove friendly buttons
GX-2009

## Slide 11
www.rkiinstruments.com
Dust and water proof, IP 67 rating
GX-2009
Notes: 11

## Slide 12
www.rkiinstruments.com
GX-2009
Dust Rating - IP 67
Subjected to talc dust vacuum chamber for 8 hours
before
after
Notes: 12

## Slide 13
www.rkiinstruments.com
GX-2009
Water Proof Rating - IP 67
Submerged in 1 meter of water
for 30 minutes
１ｍ
Notes: 13

## Slide 14
Increased data logging capacity
 | Alarm trend every 5 sec. | Interval trend | Cal. history
ＧＸ－２００１ | Before & after 15min.1event | 480 sessions | Last calibration record
ＧＸ－２００９ | Before & after 30min.8 events | 3,600 sessions | Last 100 calibration records
GX-2009

## Slide 15
www.rkiinstruments.com
GX-2009
Only a USB / IR adaptor required for
data downloading
Notes: 15

## Slide 16
www.rkiinstruments.com
GX-2009
Operates for 20 hours on
NiMH batteries
Notes: 16

## Slide 17
www.rkiinstruments.com
GX-2009
Modular gang charging, up to 5 cradles for one power source
Notes: 17

## Slide 18
Impact resistant over-mold body
GX-2009

## Slide 19
2.75” H x 2.95” W x .98” D, 4.6 oz
2.7”
GX-2009

## Slide 20
2.75” H x 2.95” W x .98” D, 4.6 oz
1”
GX-2009

## Slide 21
Low profile alligator, 360° rotation
GX-2009

## Slide 22
Replacement sensors
…and calibration cup
GX-2009

## Slide 23
www.rkiinstruments.com
Compatible with the RP-2009 attachable sample drawing pump
GX-2009
Notes: 23

## Slide 24
www.rkiinstruments.com
Air-tight IR data portal
GX-2009
Notes: 24

## Slide 25: GX-2012
Confined Space Sample Draw Monitor

## Slide 26: GX-2012
LCD
IrDA
Tapered Nozzle
Alarm Lamp 1
Buzzer (more than 95dB)
Alarm Lamp 2
Alarm Lamp 3

## Slide 27: GX-2012 Features
Monitors Lel, And % Volume Methane, Oxygen, Carbon Monoxide And Hydrogen Sulfide
0-100% Volume Methane Optional
Auto-ranging Display Of % By Volume And % Lel
Internal Sample Drawing Pump With Up To 50 Foot Range
Vibration, Visual, And Audible Alarms
Automatic Backlight During Alarms
Calibration Reminder With Lock Out Option
Lithium Or Alkaline Power Source (Interchangeable)
Quick Charge (Fully Charged In 90 Minutes)
Glove Friendly Large Buttons
Alarm Latching Or Non-latching
High Impact Protective Rubber Over Molding
Up To 600 Hours Of Data Logging With Alarm Trends
Auto Calibration Or Single Calibration
Twa And Stel Readings With Lunch-break Mode
Intrinsically Safe, Csa, C/Us Classified, Atex/IECEX Approval
IP-66 Water And Dust Resistant
2 Year Warranty

## Slide 28: Specifications
GX-2012 Model |  |  |  |  | 
Gas Detected | Combustible Gases (Methane as Standard) | % Volume Methane | Oxygen (O2) | Hydrogen Sulfide (H2S) | Carbon Monoxide (CO)
Detection Principle | Catalytic Combustion | Thermal Conductivity | Galvanic Cell | Electrochemical Cell | 
Detection Range | 0-100% LEL | 0-100% Vol. | 0-40% Vol. | 0-100 ppm | 0-500 ppm
Accuracy Statement (whichever is greater) | ± 5% of reading or ± 2% LEL | ± 5% of reading or ± 2% of full scale | ±0.5% O2 | ± 5% of reading or ± 2ppm H2S | ± 5% of reading or ± 5ppm CO
Sampling Method | Internal sample pump, flow rate monimal 0.5 LPM, includes hydrophobic filter |  |  |  | 
Display | Digital LCD with 7 segments, auto backlight during alarm |  |  |  | 
Preset Alarms (User Adjustable) | 1st Alarm 10% LEL 2nd Alarm 50% LEL Over Alarm 100% LEL | N/A | 1st Alarm 19.5% 2nd Alarm 23.5% Over Alarm 40.0% | 1st 10ppm 2nd 30ppm TWA 10ppm STEL 15ppm Over 100ppm | 1st 25ppm 2nd 50ppm TWA 25ppm STEL 200ppm Over 500ppm
Alarm Types | Gas Alarms: 1st and 2nd (user adjustable), STEL, TWA and Over Trouble Alarms: Sensor connection, low battery, low flow, circuit trouble and calibration error |  |  |  | 
Alarm Methods | Gas Alarms: Flashing lights, two tone buzzer, and vibration Trouble Alarms: Flashing lights, trouble displayed, intermittent buzzer, and vibration |  |  |  | 

## Slide 29: Alarm Types and Indications

## Slide 30: Replacing the Batteries
Turn off the GX-2012
Push the latch on the bottom of the GX-2012 toward the front of the instrument to release the battery pack
Slide

## Slide 31: Replacing the Batteries
Slide the battery pack away from the instrument
Insert a new battery pack
  Push the battery pack into the instrument until you hear a click.
Alkaline Battery Pack
Li-Ion Battery Pack

## Slide 32: Replacing the Sensors
Use a screwdriver to remove the three screws holding the flow chamber
Grab the exhaust tube and pull it gently away from the unit to slide the flow chamber out of the unit

## Slide 33: Replacing the Scrubber Filters
Place the charcoal filter over the CO sensor

## Slide 34: Replacing the Scrubber Filters
Place the H2S Scrubber over the LEL sensor

## Slide 35: Replacing the Sensors
Gently pull the tab of the sensor gasket to remove it. Be sure not to lose any of the scrubber filters that are currently installed. Note: the sensors will be exposed.
Tab
Sensor Filters

## Slide 36: Replacing the Sensors
Remove the sensors from their sockets

## Slide 37: Replacing the Sensors
Carefully insert the replacement sensor in the correct key color coded socket
GX-2012 Sensors
%Volume
Methane
Thermal Conductivity
%LEL
Catalytic
Oxygen
Carbon Monoxide
Hydrogen Sulfide

## Slide 38: Replacing the Sensors
Place the sensor gasket and filters back into the chamber ensuring that it seals with the sensors and the edge of the chamber
Ensure that the sensor filters are in place
Place the flow chamber in position over the sensor area and press it into the case until it is flush with the back of the case
Place the sensor gasket and filters back into the chamber ensuring that it seals with the sensors and the edge of the chamber.

## Slide 39: Replacing the Sensors
Place the flow chamber in position over the sensor area and press it into the case until it is flush with the back of the case.
Tighten the top screw of the flow chamber completely.
Place the belt clip into position and tighten the three screws retaining it

## Slide 40
Introducing
GX-6000
6 gas, sample draw with PID & super toxics
You Have Choices

## Slide 41
Monitor up to 6 gases
4 standard micro-sensors
2 smart sensor slots for PID, IR, & Super toxics
Library of over 600 VOC’s
Internal Sample Pump
Features
New Features
  Man-down alarm
  LED flashlight
  Panic alarm
  Auto display rotation 180

## Slide 42
IP 67
Features
New Features
Lightweight & Ergonomic
High impact rubber boot
Ergonomic design fits comfortable in hand
Operating Hours
Rechargeable – 14 hours
Alkaline – 8 hours

## Slide 43
Dimensions
7.87” (H) x 2.67” (W) x 2.04” (D)
GX-2012 = 6.81” x 2.79” x 1.69”
Weight
Approx. 400g / 14.1 ounce
GX-2012 : 360g / 12.7 ounce
2.67”
2.04”
7.87”
Compact & lightweight

## Slide 44
Glove friendly buttons can be operated with one hand
Functionality of each button is very similar to other RKI gas detectors (like GX-2012)
New functions are easily identifiable
  LED light
  Panic alarm
  Auto display rotation
Control Panel

## Slide 45
Full dot-matrix user-friendly LCD.
One of 9 languages can be selected by software.
  English, Germany, Italian, French, Portuguese, Spanish, Japanese, Korean, Russian
Display Examples
LCD Display

## Slide 46
Multi-gas view displays all 6 channels
Single gas view shows one channel in large scale with auto scrolling for each channel
Auto rotation when instrument upside down
LCD Display Options

## Slide 47
Smart sensors
PID …..PIS-00x (White)
ES …..ESS-03xx (Grey)
IR …..DES-3311-x (Black)
*Any two “smart” sensors can be combined in GX-6000, as long as PID sensor is located in the first position of gas through path.
Standard 4 gas sensors
CH4 or HC …..NC-6264A
O2 …..OS-BM2
H2S ..…ES-1827i
CO …..ES-1821
Sensors

## Slide 48
PID
Library of over 600 target gases
Iso-Butylene (C4H8) will be a standard calibration gas.
Smart Sensor Gases
*New sensors will be considered after development of above sensors.
SO2 0-6 ppm
NO2 0-9 ppm
HCN 0-15 ppm
NH3 0-75 ppm
NH3 0-400 ppm
Cl2 0-3 ppm
Cl2 0-10 ppm
EC (in order of development)
CO2 0-5% vol
HC 0-100% LEL
HC 0-30% vol
CH4 0-100% LEL
CH4 0-100% vol
CO2 0-5000 ppm
CO2 0-10000 ppm
IR

## Slide 49
Rechargeable
BUL-6000
More than 14 hours operation
Battery charger BC-6000
Alkaline
BUD-6000
AA size battery x 3 pieces
More than 8 hours operation
Power Supply

## Slide 50
Available in 2015
  New docking station can be connected to single PC (up to 10 units).
SDM-6000 Docking Station
Notes: Can be connected up to 10 units

## Slide 51
1st quarter of 2015
ATEX & IECEx is expected to be approved.
2nd quarter of 2015
The first production lot will be ready for supply.
2nd ~ 3rd quarter of 2015
The second production lot will be ready for supply.
Development Schedule