## Slide 1
Partners in Gas Detection

## Slide 2: Company Background
RKI founded in 1994
Partner company: Riken Keiki
  Leader In Gas Detection & Sensor Technology for over 75 years
California Corporation
Average employee gas detection experience is 12 years

## Slide 3: 75 Years of Milestones
1938
1969
1978
First combustible interferometer
First 2 gas monitor
LEL, O2
GX-3
First 3 gas monitor
LEL, O2, CO
Model 1641

## Slide 4: 75 Years of Milestones
1980
1982
1983
Pocket size
Single gas monitor for O2, CO or H2S
HS-80
First belt worn
3 gas
GX-82
Portable IR
For CO2
RI-411

## Slide 5: 75 Years of Milestones
1984
1986
1990
Portable IR
for Freon gases
RI-413
First belt worn
4 gas monitor
GX-86
Portable
Super Toxic
SC-90

## Slide 6: 75 Years of Milestones
1994
1995
1997
Portable 4 gas
with datalogging
and autocal
GX-94
First 6 gas portable
EAGLE
First wrist worn
GasWatch

## Slide 7: 75 Years of Milestones
2001
2003
2009
Smallest 4 gas
GX-2001
Smallest tri-mode
Portable
GX-2003
Smallest
confined space monitor
GX-2009

## Slide 8: 75 Years of Milestones
2010
2012
2016
6 gas portable
with PID capabilty
EAGLE 2
Advanced tri-mode portable
Gas Tracer / GX-2012
6 gas, sample draw with PID, IR & Super Toxics
GX-6000

## Slide 9: GX-2009
The Smallest 4 Gas Monitor Available!

## Slide 10: GX-2009
Repeat…. THE smallest 4 gas monitor available!
5” x 1.9” x 1.2”
7.8 ounces
4.1” x 2.3” x 1.4”
7.05 ounces
4.4” x 3.0” x 1.4”
8.07 ounces
4.4” x 2.4” x 1.2”
6.7 ounces
2.7” x 3” x 1”
4.6 ounces

## Slide 11: GX-2009
All gas readings displayed

## Slide 12: GX-2009
3 Large visual alarms on 3 sides

## Slide 13: GX-2009
2 audible alarms ports, 95 dB

## Slide 14: GX-2009
2 glove friendly buttons

## Slide 15: GX-2009
www.rkiinstruments.com
Dust and water proof, IP 67 rating
Notes: 15

## Slide 16: GX-2009
www.rkiinstruments.com
Notes: 16

## Slide 17: GX-2009
www.rkiinstruments.com
Dust Rating - IP 67
Subjected to talc dust vacuum chamber for 8 hours
before
after
Notes: 17

## Slide 18: GX-2009
www.rkiinstruments.com
Submerged in 1 meter of water
for 30 minutes
Water Proof Rating - IP 67
１ｍ
Notes: 18

## Slide 19: GX-2009
Increased data logging capacity
 | Alarm trend every 5 sec. | Interval trend | Cal. history
ＧＸ－２００１ | Before & after 15min.1event | 480 sessions | Last calibration record
ＧＸ－２００９ | Before & after 30min.8 events | 3,600 sessions | Last 100 calibration records

## Slide 20: GX-2009
www.rkiinstruments.com
Only a USB / IR adaptor required for
data downloading
Notes: 20

## Slide 21: GX-2009
www.rkiinstruments.com
Air-tight IR data portal
Notes: 21

## Slide 22: GX-2009
www.rkiinstruments.com
Operates for 20 hours on
NiMH batteries
Notes: 22

## Slide 23: GX-2009
www.rkiinstruments.com
Operates 14 hours after only 90 minute charge
Notes: 23

## Slide 24: GX-2009
www.rkiinstruments.com
Modular gang charging, up to 5 cradles for one power source
Notes: 24

## Slide 25: GX-2009
Impact resistant over-mold body

## Slide 26: GX-2009
2.75” H x 2.95” W x .98” D, 4.6 oz
2.7”

## Slide 27: GX-2009
2.75” H x 2.95” W x .98” D, 4.6 oz
1”

## Slide 28: GX-2009
Low profile alligator, 360° rotation

## Slide 29: GX-2009
Replacement sensors
…and calibration cup

## Slide 30: RP-2009
www.rkiinstruments.com
Compatible with the RP-2009 attachable sample drawing pump
Notes: 30

## Slide 31: SDM-2009
Stand Alone Station
Stand-alone station (no PC Required)
Charging
Calibration
Bump Test
Save Bump Test and Calibration records
Bump test and calibration records copy to USB jump drive
Includes PC software for viewing/ archiving bump test and calibration records

## Slide 32: SDM-2009
Multi Module System
Multiple modules connected to a PC (10 max)
Charging
Calibration
Bump Test
Automatic calibration/bump test option
Configure GX-2009 parameters
Archive Bump Test and Calibration records
Archive data to network location
Software controlled data retrieval
Windows 7 compatible

## Slide 33: GX-6000
6 Operating Modes of GX-6000
Normal
Leak check
Inert
Bar hole
Snap Log
Benzene Specific Mode
Monitor up to 6 Gases
H2S, CO, O2, LEL
2 smart sensor slots
  PID for VOC’s
  IR for CH4, HC, & CO2
  EC for NH3, Cl2, HCN, NO2, & SO2
PID library of more than 600 VOC’s
Accepts 10.6 and / or 10.0 PID lamps
50,000 ppb / 6,000 ppm ranges
10.0 Lamp for Benzene Specific
11.7 Lamp available Q4 2018
11.7 Lamp for carbon tetrachloride, acrylonitrile, chloroform, methanol, and refrigerants (R-143, R-132A)
PID sensors can be combined
Easily choose a target VOC
  User defined VOC list of 30
  Recently used VOC list last 8
LEL Protection mode
Shields LEL sensor from damaging VOC exposure
LCD display
Auto flip display
Peak bar graphs
Adjustable auto backlight
Customize order of gases
Single gas view with large font & auto sequence

## Slide 34: GX-6000
Weather & Dust Resistant
IP-67
Smallest 6 gas sample draw
Lightweight & Ergonomic
High impact rubber boot
Ergonomic design fits comfortable in hand
Interchangeable battery options
Lithium-ion pack operates 14 hours
  Complete recharge in 3 hours
Alkaline pack operates 8 hours
Intrinsically Safe
ATEX / IECEX
cCSAus
LED Flashlight
On demand light source
9 Languages
English, Germany, Italian, French, Portuguese, Spanish, Japanese, Korean, Russian
Alarms
2 adjustable gas alarms per channel
Man Down alarm
Panic Alarm
4 alarm LED’s
Audible and vibration alarms
Trouble alarms for low flow, sensor connection, low battery, circuit error, & calibration

## Slide 35
1. Normal Mode
6 Operating Modes of GX-6000 of GX-6000
Simultaneous gas measurement readings in real-time are shown for all the sensors installed.

## Slide 36
2. Leak Check Mode
6 Operating Modes of GX-6000
Used when performing leak checks above ground.
CH4 and CO (optional) are shown in ppm readings.

## Slide 37
3. Inert Mode
6 Operating Modes of GX-6000
Inverts the O2 alarm points to
5% vol alarm 1 and 10% vol alarm 2.
Used to alert users when there is O2 present in the area where there is supposed to be little to none.

## Slide 38
4. Bar Hole Mode
6 Operating Modes of GX-6000
Used to perform timed leak checks underground, IR combustible sensor and oxygen (if installed) are used. To be used with bar a hole probe.

## Slide 39
5. Snap Log Mode
6 Operating Modes of GX-6000
Allows the user to record data at a specific time and have it saved to the data logger. The data is assigned a snap log ID and is saved with the instrument’s station ID.

## Slide 40
6. Benzene Mode
6 Operating Modes of GX-6000
A special mode used to measure benzene gas specifically. Has to be used with the benzene
pre-filter tube and tube holder.

## Slide 41
Dimensions
7.87” (H) x 2.67” (W) x 2.04” (D)
MultiRAE= 7.6” x 3.8” x 2.6”
Weight
Approx. 400g / 14.1 ounce
MultiRAE: 880g / 31 ounce
2.67”
2.04”
7.87”
Compact & lightweight
50 % LIGHTER!

## Slide 42
LCD Display Options
Multi-gas view displays all 6 channels
Single gas view shows one channel in large scale with auto scrolling for each channel
Auto rotation when instrument upside down

## Slide 43
Peak bar graph
LCD Display Options

## Slide 44
Customize your gas readings in any order
Customize Gas Order

## Slide 45
Sensors
Standard 4 Gas Sensors
Smart Sensor
Slots

## Slide 46
Interchangeable Sensors
4 standard micro sensors are interchangeable with the 03 Series, GX-2009, GX-2012, and GX-6000
GX-2009
03 Series
GX-6000
GX-2012

## Slide 47
Smart Sensor Slots
Smart sensor slots auto-recognize any sensor you install
- No re-cal or user
setup required

## Slide 48
Smart Sensor Technology
Smart Electrochemical (ESS-03DH-XXX) | 
GAS | RANGE
Ammonia (NH3) | 0-400 ppm
Chlorine (Cl2) | 0-10ppm
Hydrogen Cyanide (HCN) | 0-15ppm
Nitrogen Dioxide (NO2) | 0-20 ppm
Sulfur Dioxide (SO2) | 0-99.9 ppm
Monitor a wide variety of toxic gases. Smart plug and play sensors are auto recognized and can be remotely calibrated | 
Photo Ionization Detection PID |  | 
GAS |  | RANGE
10.6 Lamp | 600 VOC’s | 0-50,000 ppb
 |  | 0-6,000 ppm
10.0 Lamp | Benzene Specific | 0.1-50 ppm
 | 300 VOC’s | 0-100 ppm
Monitor low ppm VOC gases. |  | 
Infrared (DES-3311-1/2) | 
GAS | RANGE
Carbon Dioxide (CO2) | 0-10,000 ppm 0-10% Vol.
Methane (CH4) | 0-100% LEL 0-100% Vol.
Hydrocarbons | 0-100% LEL 0-30% Vol.
Monitor Combustible gases in inert environments. Monitor wide range of CO2. | 

## Slide 49
Rechargeable
More than 14 hours operation
A complete charge in 3 hours
Alkaline
AA size battery x 3 pieces
More than 8 hours operation
Interchangeable Power Supply

## Slide 50
One of 9 languages can be selected by software.
  English, Germany, Italian, French, Portuguese, Spanish, Japanese, Korean, Russian
9 Languages

## Slide 51
Glove friendly buttons can be operated with one hand.
New functions are easily identifiable
  LED light
  Panic alarm
Control Panel

## Slide 52
Confined Space Entry
Applications
Monitor LEL, O2, CO, AND H2S
Pre – Entry testing with sample draw pump
-Pull samples up to 40’
-Maintain steady sample flow to sensors
Continuously monitor confined space
Utilize as a personal monitor within the confined space

## Slide 53
Environmental Monitoring
Applications
GX-6000 is Method 21 compliant
  monitor ppm level combustibles
Hazardous waste monitoring to determine proper PPE
Soil Remediation from leaking underground storage tanks
  PID measures BTEX and THC’s

## Slide 54
Leak Investigation
Applications
Common with gas supply & utility companies
Above ground leak detection utilize Leak Check Mode for ppm detection of combustible gas
  LED’s and alarm tones increase in frequency as gas concentration increases
  Audible alarm silence Perform leak investigations without alarming residents
Below ground leak investigation will use Bar hole mode for tracking leak migration

## Slide 55
Fire Industry
Applications
Hazmat Perimeter / Safe Zone verification
Emergency response to toxic gas leaks
Confined space entry / rescue
Arson Investigation
Meth lab investigation

## Slide 56
Price List Configurator

## Slide 57
  Stand alone station (no PC required)
  Bump, Calibrate, and Alarm tests
  Charge
  Touch screen menu display
  Save calibration, bump tests, alarm history and exposure data to an SD memory card or to a computer
  Automatically power on or off for scheduled maintenance
  Up to 3 ports for separate calibration gas cylinders
SDM-6000 Docking Station
Notes: Can be connected up to 10 units

## Slide 58
Multi Module System with PC Controller
  Manage up to 10 instruments with one power source, calibration source, and computer
  Configure GX-6000 parameters
  SV-3 unit expands calibration ports up to 6 ports
Notes: Can be connected up to 10 units

## Slide 59
SD / SDH Memory card slot
USB PC connection
USB Printer connection
LAN connection
Power Switch
AC adaptor
Power/Data Joint Connector
3 calibration gas ports
1 fresh air port
SDM-6000 Docking Station

## Slide 60
SDM-6000 Docking Station
  Easily connects to adjacent docks
  No extra tubing required
  Automatically distributes power, calibration gas, and data once connected
  DIN Rail wall mount

## Slide 61
GX-6000 vs MultiRAE
Similarities
Sample Draw Instruments
6 Gas Channels
PID capability
Alkaline and Rechargeable options
Man-down alarm

## Slide 62
GX-6000 vs MultiRAE
GX-6000 Advantages
Features MultiRAE’s do not have
Size: GX-6000 is half the weight of MultiRAE’s
  GX-6000 14 oz.
  MultiRAE’s 30 oz.
GX-6000 PID Advantages
  Built in VOC Library: 600 vs 190
  PID Lamp options: 10.6, 10,0, & 11.7 available in 1 instrument
  Dual PID capability: Use 2 different PID lamps simultaneously
  Wider range of VOC’s with 10.6 lamp: 6,000 vs 1,000 / 5,000 ppm
  Easy access to VOC library
    Previously Used menu stores last 8 VOC’s
    User defined list of 30 VOC’s
Smart Sensor Slots
6 Operating Modes of GX-6000:
  Normal, Leak Check, Inert Mode, Bar Hole, Snap Log, & Benzene

## Slide 63: Questions?