## Slide 1
Lithium-ion Battery Market
Introduction
World Leader in Gas Detection &
Sensor Technology

## Slide 3
Lithium Battery Production Process
Large number of instruments are used in these processes.
“Competitive”
Mixing
Coating
Drying
Calendering
Slitting
Vacuum drying
Degassing
HT aging
EOL testing
Formation
Separation
Stacking Winding
Packaging
EL filing
Electrode manufacturing
Cell assembly
Cell finishing
Gas detector
required!!
Gas detector
required!!
Gas detector
required!!
Separator manufacturing process
requires “Gas detector” as well.
Separator
Manufac.
Separator
Related activity

## Slide 5
NMP is present all the time at the coating and drying process.
Necessity of gas detection
To confirm the concentration is not decreasing
To confirm it will not exceed the explosion limit.
Coating & Drying Process
For 32GWh factory …
・around 8 lines
・around 18 sets of gas detectors per line

## Slide 6
Directly samples within the Duct
NMP volatilizes only at high temperatures.
Therefore, it is necessary to insert a detector directly into the exhaust duct and detect it at high temperature.
Coating and drying process mainly uses NMP.
It generates explosive NMP in this drying process
SD-2500 series
NMP
NMP
NMP
NMP

## Slide 7
Coater- Dryer
Responsible for the manufacturing process of electrode plates (positive and negative electrode materials), which is a key battery manufacturing process.
Suggest instrument:
1) SD-2500

## Slide 8
Model: SD-2500
Product advantage
Directly detecting inside the DUCT
Layout drawing
Advantages
1. No risk of liquefaction
⇒avoid solvent adsorption on piping and sensors.
2. Duct insert diffusion method
⇒ no dead time.
3. No suction pump required
⇒ low running cost
Accurate detection is possible because there is no risk of condensation (liquefaction)

## Slide 9
In-furnace direct feed type recommended
Riken Keiki Advantages
1) Has UL/ATEX
2) Has wide temperature range
3) Has long insert part
RIKEN KEIKI is an explosion-proof product that can be used in the highest temperature environment and has the longest insert！！
RIKEN KEIKI
- SD-2500 : 0- +160℃
- SD-2600 : 0- +200℃
UL/ATEX approval
GASTRON
- GTD-2000: -20- +60℃
New COSMOS ELECTRIC
- KD-12HT : 0- +160℃
ATEX approval
Non ATEX approval
ATEX approval
CROWCON
Xgard : -40- +150℃

## Slide 10
Competitive Advantages

## Slide 11
Lithium Battery Production Process
Large number of instruments are used in these processes.
“Competitive”
Mixing
Coating
Drying
Calendering
Slitting
Vacuum drying
Degassing
HT aging
EOL Testing
Formation
Separation
Stacking Winding
Packaging
EL Filling
Electrode manufacturing
Cell assembly
Cell finishing
Gas detector
required!!
Gas detector
required!!
Gas detector
required!!
Separator manufacturing process
requires “Gas detector” as well.
Separator
Manufac.
Separator
Related activity

## Slide 12
M2A

## Slide 13
The electrolyte contains DMC (dimethyl carbonate) and when it is vaporized, it becomes an explosive atmosphere. Also, to prevent oxygen deficiency during inspections, oxygen meter is installed.
For 1 unit of electrolyte injection system …
DMC detector：1unit＋OX-5001：1unit＋O2 detector：1unit is used
For a 32GWh factory …
・around 24 lines
・around 20 sets of gas detector per line
Model 1017F
M2A – DMC

## Slide 14
【Electrolyte injection device (image)】
We have prepared detectors that can handle each gas type.
Use : Explosion prevention /
Leakage detection（DMC）
Model : SD-D58 (DMC) /
SD-１RI (diffusion type) /
M2A
Use : Oxygen deficiency prevention
Model : SD-1 OX（diffusion type）
When DMC(dimethyl carbonate) contained in the
electrolyte is vaporized, it becomes an explosive gas.

## Slide 15
Lithium Battery Production Process
Large number of instruments are used in these processes.
“Competitive”
Mixing
Coating
Drying
Calendering
Slitting
Vacuum drying
Degassing
HT aging
EOL testing
Formation
Separation
Stacking Winding
Packaging
EL filing
Electrode manufacturing
Cell assembly
Cell finishing
Gas detector
required!!
Gas detector
required!!
Gas detector
required!!
Separator manufacturing process
requires “Gas detector” as well.
Separator
Manufac.
Separator
Related activity

## Slide 17
■Test process
“Test equipment (image)”
Use：Explosion prevention /
Poisoning prevention
(H2/CO/H2S/HF etc)
Model：GD-70D
Gas: CO, H2, H2S, HF, CH4, O2
Depending on the Type of battery (encapsulated
electrolyte), H2(hydrogen), CO(carbon monoxide),
H2S(hydrogen sulfide) occurs !!
Typically 1 or 2 gas monitors per test equipment.
Notes: Since the environment inside the test equipment is extremely harsh, it is necessary to perform pretreatment by sampling (air-cooled dehumidification, activated carbon adsorption, etc.).

## Slide 18
Lithium Battery Production Process
Large number of instruments are used in these processes.
“Competitive”
Mixing
Coating
Drying
Calendering
Slitting
Vacuum drying
Degassing
HT aging
EOL testing
Formation
Separation
Stacking Winding
Packaging
EL filing
Electrode manufacturing
Cell assembly
Cell finishing
Gas detector
required!!
Gas detector
required!!
Gas detector
required!!
Separator manufacturing process
requires “Gas detector” as well.
Separator
Manufac.
Separator
Related activity

## Slide 20
We have installation experience in Japan with ASAHI KASEI (Celgard, LLC) the No.1 separator company. Have an individual instrument that no other competitor has which was accepted by the separator company.
Separator
-> Dichloromethane is inspected while separator is manufactured.
Use：Explosion prevention /
Poisoning prevention
Model：FI-800 + RS-330
SD-1GH + Beacon Controller
GH-5001 + GD-A80V
Gas: Dichloromethane, Propane
GD-A80V
FI-800
RM-5000

## Slide 21
Major Accident Cases
Created by quoting and processing from the workplace safety site
(Ministry of Health, Labor and Welfare：http://anzeninfo.mhlw.go.jp/anzen/sai/saigai_index.html)

## Slide 22
Explosion of drying equipment while heat drying chemicals
Drying equipment cause of damage
  During the drying operation, the odor of ethanol as a solution was strongly felt and the exhaust device was confirmed. An explosion occurred after the switch was turned on because the exhaust system was not operating.
Injured : 6 people
- Thorough training of workers needed
- Establishment of safety management
system
+
- Installation of detector to detect
leakage of flammable gas

## Slide 23
Product Information

## Slide 24
Coating & Drying Processes
Flame-proof Furnace Safety Monitor
Model：SD-2500／SD-2600／GD-2400
Features
Detection of high boiling point solvents
Detection of N-methyl-2-pyrrolidone(NMP) vaporized in the drying furnace
Catch the exact concentration in the center of the exhaust duct by direct insertion in the furnace

## Slide 25
Electrolyte Filling Process
Flame-proof Suction Type Gas Detector
Model：SD-D58 | GD-D58 | M2A
Features
Suitable for use as an explosion proof product even in hydrogen atmospheres
Equipped with automatic flow rate abnormality
Integrated assemblies of replacement parts to simplify maintenance
SD-D58
(With concentration
indicator)
GD-D58
(Without concentration
indicator)
M2A
(With gas display)

## Slide 26
Testing Process
Smart Transmitter / Gas Detector
Model：GD-70D
Features
A universal design that does not depend on the sensor technology. The main unit is shared.
Reduced power consumption - up to 20% of conventional (Potentiostatic Electrolysis Method)
Compliant with GADMS and other systems
No internal tubing (Main unit) / No Coil (Pump unit)
Front access, no tools required for easy replacement of sensor & pump

## Slide 27
Personal Safety | Confined Space | VOC Detection
Portable Gas Monitors
Model：GX-3R | GX-3R Pro | GX-6000
GX-3R
- Smallest confined space monitor
GX-3R Pro
- Smallest 5 gas monitor
- Bluetooth alarm notifications
GX-6000
- 6 gas sample draw with
smart sensors
- 4 PID sensor options
- 5 operating modes

## Slide 28
SUCCESSES

## Slide 29
Panasonic Energy of North America

## Slide 30
Equipment | Model | Gases | Ranges | Units
Liquid injection device | M2A（IR Type） | DMC | 0-100％LEL | 200
Liquid injection device | OX-5001-1017 | O2 | 0-25VOL% | 200
GNC Device | M2A（IR Type） | DMC | 0-100％LEL | 200
GNC Device | OX-5001-1017 | O2 | 0-25VOL% | 200
Encapsulation device | GP-6001-1017 | Xylene, Hexane | 0-100％LEL | 10
Coater machine | GP-5001-A2400 | NMP | 0-100％LEL | 126
Li-Ion Manufacturing Shipments

## Slide 31
Gas sensor deterioration factors
In principle, the gas sensor detects gas by a chemical quantitative reaction.
Contact with substances that are chemically harmful to the sensor
Due to changes in the properties of sensor constituent materials due to long-term use
Its sensitivity is gradual, but it deteriorates.
Sensitivity confirmation by regular inspection and regular replacement as preventive maintenance are required
Deterioration factors of constant potential electrolytic sensor
■ Working electrode [Reduction of surface area]
⇒ Impurity mixed (surface oxidation / dissolution)
⇒Long-term contact with reaction gas (surface oxidation)
■ Gas permeable membrane [Reduction of transmittance]
⇒ Adhesion of fine particles, oil misto, etc. (clogging)
⇒ Organic solvent vapor contact (decreased water repellency)
⇒ Pressure load (decreased water repellency)
■ Electrolyte [Reduction of liquid volume]
⇒ Dry air contact (electrode exposure)
Deterioration factors of constant potential modulus sensor
■ Working electrode [Reduction of surface area]
⇒ Impurity mixed (surface oxidation / dissolution)
⇒Long-term contact with reaction gas (surface oxidation)
■ Gas permeable membrane [Reduction of transmittance]
⇒ Adhesion of fine particles, oil misto, etc. (clogging)
⇒ Organic solvent vapor contact (decreased water repellency)
⇒ Pressure load (decreased water repellency)
■ Electrolyte [Reduction of liquid volume]
⇒ Dry air contact (electrode exposure)
Gas permeable membrane

## Slide 32
Need for maintenance
---------- Specificity of gas detector equipment ----------
To operate correctly in case of emergency
Maintenance of functions and performance is extremely important
■ The detection target is gas →
There is no operation inspection method other than gas introduction
■ The usage environment is complicated and diverse →
There is a "difference" in the operating status (due to the environment)
■ Normally, it is in a standby state (it never operates) →
There is almost no opportunity to check the operation
Maintaining durability in continuous operation.
Regular inspection and maintenance

## Slide 33
N-Methyl-2-pyrrolidinone(NMP) Physical properties
Chemical formula : C5H9NO
Molecular weight : 99.13
Lower explosion limit : 0.9 vol%
Flash point : 95 ℃
-> Exceeding this may produce air and
explosive gas mixtures
Boiling point : 204 ℃
Vapor pressure : 66 Pa(25 ℃) -> 7 %LEL
3200Pa(=3.2kPa)->350 %LEL(3.15 vol%)
Classification : Corresponds to third petroleum
Structure formula

## Slide 34
Dimethyl carbonate(DMC) Physical properties
Chemical formula : C3H6O3
Molecular weight : 90.08
Lower explosion limit : 4.2 vol%
Flash point : 18 ℃
-> Exceeding this may produce air and
explosive gas mixtures
Boiling point : 90.2 ℃
Vapor pressure : 7.4 kPa(25 ℃) -> 173 %LEL(7.3 vol%)
Classification : Corresponds to first petroleum
Structure formula