## Slide 1
GX-3R and GX-3R Pro Safeware Product Introduction
Evolution In Gas Detection

## Slide 2: 2 Models—Depending on Need
Standard 4-gas model
GX-3R
Worlds smallest and lightest 4-gas monitor
Low cost of ownership
GX-3R Pro
  4-gas plus extra slot for toxic or IR sensor
  Wireless communication with mobile app
  Man-down and panic alarms
  Alkaline/Rechargeable option
Pro 5-gas model

## Slide 3
2.2” x 2.55” x 1”
3.7 ounces
GX-3R
The NEW Smallest and Lightest 4-gas Monitor
Advancements from GX-2009
Size & Weight
Smallest
— Meet Smaller!
3” x 2.7” x 1”
4.6 ounces
GX-2009

## Slide 4
GX-3R Pro
2.9” x 2.6” x 1.06”
4.6 ounces
Advanced 5-gas version is the same size as GX-2009
Advancements from GX-2009
Size & Weight
3” x 2.7” x 1”
4.6 ounces
GX-2009

## Slide 5: Size Matters In the “Breathing Zone”
“The breathing zone is within a ten inch radius of the worker's nose and mouth. OSHA requires that worker exposure monitoring air samples be collected in the breathing zone. Air sampling filters may be attached to the collar or lapel.”
The GX-3R and GX-3R Pro’s small size enables them to easily be clipped into the “Breathing Zone.”
Source: https://webapps.dol.gov/elaws/osha/lead/glossary.asp#breathingzone

## Slide 6: Competitor Comparison
Size & Weight
5.12” x 1.9” x 1.8”
8 ounces
4.1” x 2.3” x 1.4”
6.4 ounces
4.4” x 3.0” x 1.4”
7.9 ounces
2.2” x 2.55” x 1”
3.7 ounces
2.9” x 2.66” x 1.06”
4.6 ounces
4.4” x 2.4” x 1.2
6.3 ounces
4.7” x 2.7” x 1.2”
7.67 ounces
The GX-3R weighs about half of the average 4-gas detector!

## Slide 7
Sensor Advancements
GX-3R Pro
4 Sensors slots for 5 gas channels
GX-3R
3 Sensors slots for 4 gas channels
CO/H2S
Dual Sensor

## Slide 8
All gas readings displayed
CO – Carbon Monoxide
Dual sensor for CO and H2S in one channel
The GX-3R simultaneously monitors:
Dual filament design gives added silicone poisoning resistance to LEL sensor
Eliminate H2 interference with CO readings with optional H2 compensated O2 sensor
H2S – Hydrogen Sulfide
LEL – Combustibles
and O2 – Oxygen
H2 compensated CO sensor available
Lead free electro-chemical sensor design gives O2 sensor a 3-5 year lifespan
Sensor Advancements

## Slide 9
CO – Carbon Monoxide
Simultaneously monitor the four standard gases
H2S – Hydrogen Sulfide
LEL – Combustibles
O2 – Oxygen
And Toxics
H2 compensated CO sensor available
EC sensor for SO2 (0-100 ppm)
IR sensor can monitor CO2 in ppm or % vol. HCN, NO2, NH3 and Cl2 planned for 2020
5th channel for toxic and IR sensors
Toxic Channel Options
Sensor Advancements
GX-3R Pro

## Slide 10
Easily identify workers using instruments that have not been calibrated, bump tested, or have been in alarm.
Red LED’s flash every 30 seconds.
Non-compliance Indicator
Non-compliance indicator in both GX-3R and GX-3R Pro

## Slide 11: Advancements
Calibration Stations
SDM-2009
Bump Time: 10 seconds
Gas Consumption: 450 ml / min
Output: USB drive / USB Cable to PC
Bump Time: 10 seconds
Gas Consumption: 250 ml / min (About 50% less gas usage than SDM-2009)
Output: Internal memory / USB drive / LAN cable / USB Cable to PC
Accepts both GX-3R and GX-3R Pro
SDM-3R

## Slide 12: Advancements
Clip-on Pump Unit
RP-2009
Flow rate: 450ml / min
Distance to draw: 50 feet
Operation time: 8h
Operation mode: Normal mode only
RP-3R
Flow rate: 500ml / min
Distance to draw: 50 feet
Operation time: 10h
Operation mode: Normal mode, Eco mode
Fits both GX-3R and GX-3R Pro

## Slide 13: More Advancements
 | GX-2009 | GX-3R and GX-3R Pro
Battery life (continuous) | 20 hours | 24 hours*
Temperature Range | -4°F to 122°F | -40F° to 140°F
Calibration Cup | Not included | Ships standard
IP Rating | IP67 | Both units IP66 & IP68
Warranty | 2 years | 3 years (device & sensors)
Durability | 1 meter drop tested | 7 meter drop tested
User Adjustable Alarms | 2 | 3
Stealth Mode | no | yes – (great for LE applications)
*GX-3R Pro has alkaline option available (16 hour battery life)

## Slide 14: GX-3R Pro—Connectivity
RK Link App
Bluetooth connectivity
Direct readings from instrument
Digital values/Graphical display
Alarm indications
Set bump/cal reminders, alarm parameters, and other GX-3R Pro settings
Configure alarm notifications to desired contacts
Find my instrument feature
Available on iOS and Android

## Slide 15: Configurable Alarm Notifications
Configure who you want to receive your alarm notifications
Configure which types of alarms you want notifications sent for
GX-3R Pro—Connectivity

## Slide 16: Alarm Location
And uses your phone’s GPS location to notify your contacts where the alarm occurred
*SMS notifications available on Android only
GX-3R Pro—Connectivity
The RK Link app notifies your assigned contacts when it goes into alarm
by text
by e-mail

## Slide 17: GX-3R Pro—Alarms
User can trigger instrument into alarm by tapping it twice to notify others of an immediate hazard.
Panic Alarm
Man Down Alarm
Man-down alarm sounds if no motion is detected for 30 seconds, increasing worker safety.

## Slide 18
OPERATION

## Slide 19
Turn on the GX-3R and GX-3R Pro by pressing and holding the POWER MODE button
Turn on
GX-3R
GX-3R Pro

## Slide 20
Press AIR button to continue without performing a calibration
GX-3R Cal Reminder
Acknowledge and use
Perform a calibration
If calibration is due, press the POWER/MODE button to perform calibration.

## Slide 21
If calibration is due, press the POWER/MODE button to perform calibration.
GX-3R Pro Calibration Reminder
Acknowledge and use
Perform a calibration
Calibration Menu is located in User Mode
Press AIR button to continue without performing a calibration.

## Slide 22
If bump is due, press the POWER/MODE button to perform bump.
GX-3R Pro Bump Reminder
Acknowledge and use
Perform a Bump Test
Bump Test Menu is located in User Mode
Press AIR button to continue without performing bump.

## Slide 23
Several seconds after warm-up, these are the normal operating mode screens for the GX-3R and GX-3R Pro
Normal Mode
GX-3R
GX-3R Pro

## Slide 24
Please make sure you are in a fresh air environment prior to zeroing your reading!
Fresh Air
GX-3R
GX-3R Pro
To perform a fresh air adjustment press and hold the AIR button

## Slide 25
Release the AIR button when it prompts you to release it
Fresh Air
GX-3R
GX-3R Pro

## Slide 26
Once the reading goes back to normal,
press the POWER/MODE button to silence the unit.
Alarm Condition
GX-3R
GX-3R Pro
If you are in alarm, get to a safe location.

## Slide 27
Display Mode vs. Normal Operation
PEAK
STEL
TWA
HC GAS LIST
USER ID
STATION ID
CAL DATA
BUMP DATA
DATE
ALARM POINTS
INVERT SELECT
LCD BACKGROUND
BLUETOOTH
BUZZER VOLUME
LANGUAGE
To enter Display Mode, press POWER/MODE button
Continue pressing the POWER/MODE button to scroll through Display Mode menu options

## Slide 28
Display Mode menus differ slightly in your GX-3R and GX-3R Pro.
Display Mode vs. Normal Operation
PEAK
STEL
TWA
LIST
USER ID
STN ID
CAL DATA
BUMP DATA
TEMP
ALARM-PT
You will know you are in display mode if you see a display mode menu title on the bottom of your screen
To return to normal operation, scroll all the way through the display menus, or wait 20 seconds and the unit will automatically return to normal mode

## Slide 29
Turn off the GX-3R and GX-3R Pro by pressing and holding the POWER MODE button
Turn off
GX-3R
GX-3R Pro

## Slide 30
SDM-3R

## Slide 31
SDM-3R: GX-3R Placement
When placing the GX-3R into the docking station, remember to have the yellow tab in the upright position.

## Slide 32
SDM-3R: GX-3R Pro Placement
The yellow tab needs to be in the down position to accept the GX-3R Pro.

## Slide 33
SDM-3R: Gas Ports
Air port
Gas 1
Gas 2
Gas 3
Three gas inputs available

## Slide 34
Steve’s daisy-chain poster?

## Slide 35
SDM-3R: USB port
USB port
USB port for downloading local data

## Slide 36
SDM-3R: Rear ports
AC power
Ethernet
PC Connection