## Slide 1
GX-3R and GX-3R Pro Product Introduction
Evolution In Gas Detection

## Slide 2: 2 Models—Depending on Need
Standard 4-gas model
GX-3R
Worlds smallest and lightest 4-gas monitor
Low cost of ownership
GX-3R Pro
  4-gas plus extra slot for toxic or IR sensor
  Wireless communication with mobile app
  Man-down and panic alarms
  Alkaline/Rechargeable option
Pro 5-gas model

## Slide 3
2.2” x 2.55” x 1”
3.7 ounces
GX-3R
The NEW Smallest and Lightest 4-gas Monitor
Advancements from GX-2009
Size & Weight
Smallest
— Meet Smaller!
3” x 2.7” x 1”
4.6 ounces
GX-2009

## Slide 4
GX-3R Pro
2.9” x 2.6” x 1.06”
4.6 ounces
Advanced 5-gas version is the same size as GX-2009
Advancements from GX-2009
Size & Weight
3” x 2.7” x 1”
4.6 ounces
GX-2009

## Slide 5: Size Matters In the “Breathing Zone”
“The breathing zone is within a ten inch radius of the worker's nose and mouth. OSHA requires that worker exposure monitoring air samples be collected in the breathing zone. Air sampling filters may be attached to the collar or lapel.”
The GX-3R and GX-3R Pro’s small size enables them to easily be clipped into the “Breathing Zone.”
Source: https://webapps.dol.gov/elaws/osha/lead/glossary.asp#breathingzone

## Slide 6: Competitor Comparison
Size & Weight
5.12” x 1.9” x 1.8”
8 ounces
4.1” x 2.3” x 1.4”
6.4 ounces
4.4” x 3.0” x 1.4”
7.9 ounces
2.2” x 2.55” x 1”
3.7 ounces
2.9” x 2.66” x 1.06”
4.6 ounces
4.4” x 2.4” x 1.2
6.3 ounces
4.7” x 2.7” x 1.2”
7.67 ounces
The GX-3R weighs about half of the average 4-gas detector!

## Slide 7
Sensor Advancements
GX-3R Pro
4 Sensors slots for 5 gas channels
GX-3R
3 Sensors slots for 4 gas channels
CO/H2S
Dual Sensor

## Slide 8
All gas readings displayed
CO – Carbon Monoxide
Dual sensor for CO and H2S in one channel
The GX-3R simultaneously monitors:
Dual filament design gives added silicone poisoning resistance to LEL sensor
Eliminate H2 interference with CO readings with optional H2 compensated O2 sensor
H2S – Hydrogen Sulfide
LEL – Combustibles
and O2 – Oxygen
H2 compensated CO sensor available
Lead free electro-chemical sensor design gives O2 sensor a 3-5 year lifespan
Sensor Advancements

## Slide 9
Sensor Advancements
Interference Gas Scrubber Disc
Gas scrubber disc’s are replaceable, lowering cost by eliminating need to replace entire sensor

## Slide 10
CO – Carbon Monoxide
Simultaneously monitor the four standard gases
H2S – Hydrogen Sulfide
LEL – Combustibles
O2 – Oxygen
And Toxics
H2 compensated CO sensor available
EC sensor for SO2 (0-100 ppm)
IR sensor can monitor CO2 in ppm or % vol. (available 8/19)
HCN, NO2, NH3 and Cl2 planned for 2020
5th channel for toxic and IR sensors
Toxic Channel
Sensor Advancements
GX-3R Pro

## Slide 11
Easily identify workers using instruments that have not been calibrated, bump tested, or have been in alarm.
Red LED’s flash every 30 seconds.
Non-compliance Indicator
Non-compliance indicator in both GX-3R and GX-3R Pro

## Slide 12: Advancements
Calibration Stations
SDM-2009
Bump Time: 10 seconds
Gas Consumption: 450 ml / min
Output: USB drive / USB Cable to PC
Bump Time: 10 seconds
Gas Consumption: 250 ml / min (About 50% less gas usage than SDM-2009)
Output: USB drive / LAN cable / USB Cable to PC
Accepts both GX-3R and GX-3R Pro
SDM-3R

## Slide 13: Advancements
Clip-on Pump Unit
RP-2009
Flow rate: 450ml / min
Distance to draw: 50 feet
Operation time: 8h
Operation mode: Normal mode only
RP-3R
Flow rate: 500ml / min
Distance to draw: 50 feet
Operation time: 10h
Operation mode: Normal mode, Eco mode
Fits both GX-3R and GX-3R Pro

## Slide 14: More Advancements
 | GX-2009 | GX-3R and GX-3R Pro
Battery life (continuous) | 20 hours | 24 hours*
Temperature Range | -4°F to 122°F | -40F° to 140°F
Calibration Cup | Not included | Ships standard
IP Rating | IP67 | Both units IP66 & IP68
Warranty | 2 years | 3 years (device & sensors)
Durability | 1 meter drop tested | 7 meter drop tested
User Adjustable Alarms | 2 | 3
Stealth Mode | no | yes – (great for LE applications)
*GX-3R Pro has alkaline option available (16 hour battery life)

## Slide 15: GX-3R Pro—Connectivity
RK Link App
Bluetooth connectivity
Direct readings from instrument
Digital values/Graphical display
Alarm indications
Set bump/cal reminders, alarm parameters, and other GX-3R Pro settings
Configure alarm notifications to desired contacts
Find my instrument feature
Available on iOS and Android

## Slide 16: Configurable Alarm Notifications
Configure who you want to receive your alarm notifications
Configure which types of alarms you want notifications sent for
GX-3R Pro—Connectivity

## Slide 17: Alarm Location
And uses your phone’s GPS location to notify your contacts where the alarm occurred
GX-3R Pro—Connectivity
The RK Link app notifies your assigned contacts when it goes into alarm
by text*
by e-mail

## Slide 18: GX-3R Pro—Alarms
User can trigger instrument into alarm by tapping it twice to notify others of an immediate hazard.
Panic Alarm
Man Down Alarm
Man-down alarm sounds if no motion is detected for 30 seconds, increasing worker safety.

## Slide 19: Questions?