## Slide 1
Digester Gas Monitor System

## Slide 2: The big picture

## Slide 3: The big picture

## Slide 7: What is a biogas plant?

## Slide 8: What is cogeneration?

## Slide 9: What is a digester?

## Slide 10: Gas treatment

## Slide 11: Gas treatment
Pre Scrubber Digester
Post Treatment Aspirator

## Slide 12: Food Waste Digester

## Slide 13: Applications
Wastewater treatment plants
Landfills
Dairy farms
Poultry processing
Agricultural waste
Animal farm “lagoons”
Food waste processors

## Slide 14: Reasons for monitoring
Customer wants to use digester-produced gas to run an engine to generate electricity
Gas is typically high humidity and high H2S content
H2S will damage engine, so level must be controlled, typically by scrubber
Customer will want to check H2S at intake and exhaust from scrubber

## Slide 15: Reasons for monitoring
Customer may also want to detect methane level of gas, to determine quality
Customer may also want to detect O2 level of gas, to prevent an explosion, verify process, and make sure no air is leaking into process
CO2 content can also be checked

## Slide 16: Detectable Gases
Accurately measure high levels of H2S
Up to 4 sensors
  Methane 0-100% Volume
  CO2 0-50% Volume
  Oxygen 0-25% Volume
  H2S 0-1000 PPM 0-3,000 or 5,000 optional

## Slide 17: Features and Benefits
Sample system handles high humidity
100 ft. sample range
Self draining moisture trap
Automatic back-flush of sampling system
Long life air aspirator (no moving parts)
Corrosion resistant design, NEMA 4X enclosure

## Slide 18: Features and Benefits
Three-stage moisture/humidity control
High range H2S detection (up to 5000 ppm)
Infrared sensors for methane and CO2 detection
Automatic zero adjustment
Rugged aspirator-based sampling system

## Slide 19: Features and Benefits
Optional horn/strobe
User adjustable cycle interval from 15 minutes to 24 hours
Durable IR sensors for methane and CO2 detection
Long-life partial pressure O2 sensor

## Slide 20: Component Detail

## Slide 21: Component Detail

## Slide 22: Flow Diagram

## Slide 23: Post Treatment Panel
Monitor H2S Scrubber Exhaust for H2S
Alerts when it’s time to change H2S scrubber
Protects digester generator engine

## Slide 24: Post Treatment Panel Detail
M2 for H2S
M2 for CH4
Dilution flow meter
Regulator for compressed air supply
Aspirator
Blow–out valve
Water/particulate filter
(self draining)
Low flow switch
Sample flow
Calibration valve

## Slide 25
Web link to map of US Biogas Locations

## Slide 26
Digester YouTube Video Calibration
Click on the image

## Slide 27: Questions?