## Slide 1
Beacon 3200 Model

## Slide 2: Applications
Petrochemical plants
Water & wastewater treatment plants
Gas, telephone, & electric utilities
Steel
Refineries
Pulp & paper mills
Parking garages
Industrial plants

## Slide 3: 8 Sensor / Relay Modules
8 card slots for sensors (4 channels per card) or relays (8 relays per card)
Maximum 32 channels (but no relay cards in this case)
Examples of sensor/relay combos:
  4 sensors cards (16 channels), 4 relay cards (32 relays)
  4 common relays
Sensor card installed
Relay card installed

## Slide 4: Touchscreen Display
Control up to 32 gas monitoring channels
7” Color touchscreen display of all 32 channels
Accepts LEL / O2 / CO2 / toxic direct connect sensors

## Slide 5: Touchscreen Display

## Slide 6: Touchscreen Display

## Slide 7: Enclosure
NEMA 4 X
9 Conduit wiring hubs, ¾” NPT
Power options – 115 VAC / 220 VAC / 24VDC
Operating temperature -40F to 122F
  Optional Accessories
  Battery backup assembly
  Strobe light
Reset switch

## Slide 8: Compatible Transmitters
Any 4-20 mA transmitters, 2 or 3 wire
  S2 | M2A | T2A | T3A | VOC Pro | GD-70D | SD-1
Direct connect sensors

## Slide 9: Communications
  Modbus Slave
  Modbus Master (for M2A, T3A, VOC Pro, Air Alert)
  Ethernet Slave
  4-20 mA output for each channel
  4-20 mA input for each channel
  On board relays and relay cards, all configurable
  Touch panel LCD for user interface
  Audible alarm with silence feature
  Optional top mounted strobe light
  SD Card for datalogging

## Slide 10: Interior Detail

## Slide 11: Component Detail

## Slide 12: Questions?