## Slide 1
T2A
How to install panel widening ring

## Slide 2
Remove the enclosure lid

## Slide 3
Pull the panel off as shown

## Slide 4
Remove the two upper screws behind the circuit board to remove the front red panel

## Slide 5
Separate the front red panel from the circuit board

## Slide 6
Align the black widening ring properly to the front red panel as shown above

## Slide 7
Tighten the two bolts with washer and nut

## Slide 8
Align the three buttons on the circuit board to the back of the red panel

## Slide 9
Reinstall the upper screws

## Slide 10
Align the two prongs to the back of the unit and push down until firmly seated

## Slide 11
Reinstall the enclosure lid