## Slide 1: The GX-3R The World’s Smallest 4-Gas Detection Unit
Evolution In Gas Detection

## Slide 2: The GX-3R The Smallest and Lightest 4-gas Monitor
H: 2.55”
W: 2.2”
D: 1.02”
And it weighs only 3.52 ounces!

## Slide 3: Size Matters In the “Breathing Zone”
“The breathing zone is within a ten inch radius of the worker's nose and mouth. OSHA requires that worker exposure monitoring air samples be collected in the breathing zone. Air sampling filters may be attached to the collar or lapel.”
GX-3R
So small and light, the GX-3R clips comfortably in the breathing zone.

## Slide 4: Simultaneously Monitor 4 Gasses
All gas readings displayed
CO – Carbon Monoxide
Dual sensor for CO and H2S in one channel
The GX-3R monitors:
Dual filament design gives added silicone poisoning resistance to LEL sensor
Eliminate H2 interference with CO readings with optional H2 compensated O2 sensor
H2S – Hydrogen Sulfide
LEL – Combustibles
and O2 – Oxygen
GX-3R
(H2 compensated CO sensor available)
Lead free electro-chemical sensor design gives O2 sensor a 3-5 year lifespan

## Slide 5: Sensors
GX-3R
Sensors are field replaceable
(as easy as changing a clock battery)
Can be configured with interchangeable combos to detect a multitude of gasses
Long-lasting with a 3-year warranty

## Slide 6
GX-3R
Easily identify workers using instruments that have not been calibrated, bump tested, or have been in alarm. Red LED’s flash every 30 seconds.
Non-compliance Indicator

## Slide 7: Large LCD Auto-backlit Display
Full dot LCD display is easy to read even in adverse conditions
GX-3R

## Slide 8: Concussion Resistant
The GX-3R has been drop-tested from over 23 feet.
It can handle the conditions of your rugged work environment
GX-3R

## Slide 9: Removable Rubber Boot
The removable rubber boot adds impact protection, can be removed when cleaning and replaced if necessary.
GX-3R
Low profile alligator clip rotates 360°. Comfortably view the instrument display from a variety of positions.
Alligator Clip

## Slide 10: IP-66 / IP-68 Rating
GX-3R
The GX-3R is IP-66 rated because it can withstand jets of water
It is also IP-68 rated because it can withstand submersion in water
Critical for withstanding harsh industrial environments
The first digit shows that it is dust proof
The second digit shows it is waterproof

## Slide 11: 3 Year Warranty
The GX-3R has a 3 year warranty
GX-3R
The warranty covers workmanship of the device
AND the sensors.

## Slide 12: 3 Adjustable Alarm Levels
Three adjustable alarm points let you customize your instrument to fit your needs.
GX-3R
Revert back to standard factory settings any time.

## Slide 13: 3 Alarm Types
Visual LED light indicators Alert you to gas, low battery, and failure alarms
Audible 95 decibel buzzer Buzzer sounds for gas alarms, malfunctions, low battery voltage, and as an indicator
Vibration An internal motor vibrates for gas alarms, unit malfunctions, and as an indicator
GX-3R

## Slide 14: 2 Button Operation
2 Glove -friendly Buttons
GX-3R
Easy to use!

## Slide 15
GX-3R
Rechargeable Lithium-Ion Battery
Lithium Ion battery gives 25 hours of continuous operation minutes, with a complete recharge in 90.
It has an easy and convenient charging cable, no cradle required!

## Slide 16: SDM 3R Calibration Station
GX-3R
Charge, bump test, calibrate and alarm test instruments using less calibration gas
Automatically schedule tests
Bank up to 10 units with tubeless connection
Access instrument data via USB or ethernet

## Slide 17: High Capacity Data Logging
The GX-3R automatically logs data every 5 minutes for 300 hours of measurement. (note: logging interval can be changed in settings)
Infrared Communication Port
Transfer data from the instrument to a PC with a USB/IR adaptor, no cradle required.
GX-3R

## Slide 18: RP-3R Sampling Pump
GX-3R
Clip-on sampling pump has a 50’ range and independent power supply
Continuously operates for 10 hours
Eco mode will operate up to 16 hours

## Slide 19: Lunch Break Mode
GX-3R
Retain TWA and PEAK values from last use to pick up where you left off.
Stealth Mode
Set the alarm to notify silently—perfect for law enforcement and other applications

## Slide 20: Low Cost of Ownership
The GX-3R is a complete instrument. It is easy to maintain and is NOT disposable.
Long lasting sensors, low parts replacement costs, plus a history of long-term product support makes this the best value of any 4-gas instrument
GX-3R

## Slide 21: 9 Languages
GX-3R
Available in 9 languages:
English
日本語 (Japanese)
Español (Spanish)
Deutsch (German)
Français (French)
Italiano (Italian)
Pусский (Russian) 中文 (Chinese)
한국어 (Korean)

## Slide 22: The GX-3R
GX-3R

## Slide 23: 2 Models—Depending on Need
Compliance 4-gas model
GX-3R
Worlds smallest and lightest 4-gas monitor
Impact, water, & dust resistant
3 year Warranty
GX-3R Pro
  4-gas plus extra slot for toxic or IR sensor
  Wireless communication with mobile app
  Man-down and panic alarms
  Alkaline/Rechargeable option
5-gas pro model

## Slide 24
GX-3R