## Slide 1: GX-6100 6 Gas Sample Draw PID / IR / TC / MOS & Super Toxic Sensors

## Slide 2: The GX-6100 delivers everything the GX-6000 offered — AND SO MUCH MORE!
Next-generation handheld 6-gas detector
Advanced smart sensor technology
Longest battery runtime in its class
Enhanced alarms for maximum safety
Wireless connectivity for real-time alert sharing

## Slide 3
R sensors with 3-year warranty
  Interchangeable with the GX-3R, GX-3R Pro, and GX-Force
Smart sensors for wide gas detection range
  Humidity-resistant PID sensors
  Electrochemical sensors for toxic gases
  IR sensors for combustibles and CO2
TC sensors measure % volume combustibles
  Interchangeable with the GX-2003, GX-2012, and Gas Tracer
MOS sensors detect methane and isobutane in PPM
Sensor Technology
6 Sensors slots for 7 gas channels
Dual Sensor

## Slide 4
Detects:
  CO2, SO2, NO2, HCN, Cl2, NH3, PH3
Expanded combustible gas detection range:
  PPM
  % LEL
  % Vol.
Sensor Technology
Smart Electrochemical (ESS-03DH-XXX)
Monitor a wide variety of toxic gases. Smart plug and play sensors are auto recognized and can be remotely calibrated
Photo Ionization Detection PID
Monitor low ppm VOC gases.
Infrared (DES-3311-1/2)
Monitor Combustible gases in inert environments. Monitor wide range of CO2.
O2 Sensor
Dual CO/H2S Sensor
LEL Sensor
TC / MOS Sensor

## Slide 5
4 PID lamp options:
  10.0 eV
  10.6 eV (low/high)
  11.7 eV
Dual PID configuration possible
Built-in library of 600+ VOCs
Favorites list: 30 VOCs
Recent VOC history:
  8 most recent
Benzene-specific mode with pre-filter tube
PID & VOC Library

## Slide 6
28 hours runtime with Li-ion battery pack
  Recharges in 6 hours
8 hours runtime with alkaline battery pack
Interchangeable, field-replaceable packs
Minimizes downtime during critical operations
Power & Battery
Rechargeable
Alkaline

## Slide 7
User Interface & Display
Large LCD with auto backlight
Auto display rotation for readability
Peak-bar display shows hazard spikes
Customizable order of gases displayed
Supports 15 additional languages for global use:
  Japanese, Korean, Chinese (simplified & traditional), Vietnamese, Italian, Spanish, Slovak, Czech, German, Turkish, French, Portuguese, Polish and Russian

## Slide 8
Gas alarms:
  Alarm 1, Alarm 2, Alarm 3, TWA, STEL
Panic alarm for emergencies
Man-down alarm detects immobility
LEL sensor protection mode
Visual alarms:
  5 LEDs on 3 sides
95 dB audible alarm + vibration alerts
Alarm Systems

## Slide 9
Bluetooth Low Energy for rapid alert sharing
Integrates with RK Link software
Bluetooth and RK Link

## Slide 10
Impact-resistant removable rubber boot
Dust and water resistant enclosure (IP-67)
Field-replaceable sensors, filters, and pump
Temperature range:
  -20°C to +50°C
Explosion-proof approvals:
  ATEX, IECEx, TIIS
Durability

## Slide 11
Battery life
GX-6100 vs GX-6000
28 hours ✅ | 14 hours
✅ | -
✅ | -
✅ | -
✅ | -
15 ✅ | 8
3 years ✅ | 2 years
CO(-H2)
TC Sensor
Languages
Warranty
GX-6100
GX-6000
Bluetooth
MOS Sensor

## Slide 12
Gases
GX-6100 vs GX-2012
6 ✅ | 4
VOCs, CO2, SO2, NO2, HCN, PH3, Cl2 ✅ | Standard 4 gases plus TC
✅ | -
✅ | -
28 hours ✅ | 10 hours
✅ | Standard alarm
15 ✅ | English only
Additional Gases
Benzene
Battery
Man-down / Panic Alarm
GX-6100
GX-2012
Bluetooth
Languages

## Slide 13
Confined Space Entry
Monitor LEL, O2, CO, AND H2S
Internal sampling pump for pre-entry
  Pull samples up to 100’
  Maintain steady sample flow to sensors
Audible, visual and vibration alarms
Man down alarm
Panic alarm
Applications

## Slide 14
VOC Monitoring
Applications
10.6, 11.7 and 10.0 PID lamps available
PID library of over 600 VOCs
Two ranges available for 10.6 lamp
  0-40,000 ppb or 0-4,000 ppm
10.0 Lamp for Benzene Specific
11.7 Lamp for carbon tetrachloride, acrylonitrile, chloroform, methanol, and refrigerants (R-143, R-132A)
PID sensors can be combined

## Slide 15
Leak Investigation
Applications
Provides ppm detection of combustible gas
Bar hole mode for tracking leak migration
Leak check mode with audible/visual feedback
  LED’s and alarm tones increase in frequency as gas concentration increases
Audible alarm silence
  Perform leak investigations without alarming residents
Man down alarm

## Slide 16
Fire Industry
Hazmat Perimeter / Safe Zone verification
Emergency response to toxic gas leaks
Confined space entry / rescue
Arson Investigation
Meth lab investigation
Applications

## Slide 17
SDM-6100
  Available Q2 2026
  Stand alone station (no PC required)
  Bump, Calibrate, and Alarm test
  Charge
  Touch screen menu display
  Save calibration, bump tests, alarm history and exposure data to a USB drive or to a computer
  Automatically power on or off for scheduled maintenance
  Up to 3 ports for separate calibration gas cylinders

## Slide 18
GX-6100 vs Competitors

## Slide 19
Questions?